## Slide 1
​
Group -11
2210176143 - Md Fayed Hasan
2110676137 - Momin Sarker
2110476113 - Md Shamim Reza
2110276105 - Md ​Shamiur Rahman Sefat

## Slide 2: Topic
ADC with DMA, Analog Watchdog & Bit-Banding
Advanced Autonomous Monitoring System

## Slide 4: Traditional CPU-Based Monitoring
Software Polling Method:
while(1) {
ADC_Start();
while(!ADC_Complete()); // CPU Stuck Here
value = ADC_Read();
if(value > THRESHOLD)
Alarm();
}
Problems: • High CPU usage • Latency • Non-deterministic timing

## Slide 5: Hardware-Assisted Architecture
Sensor ↓ ADC (Continuous) ↓ DMA (Circular) ↓ SRAM Buffer
Parallel: Analog Watchdog → Interrupt

## Slide 6
• 12-bit SAR ADC • Up to 1 Msps • 16 channels • Scan Mode • Continuous Mode • External trigger support
ADC Engine

## Slide 7: Sample Time vs Conversion Time
Tconv = Tsample + 12.5 ADC cycles
Example:
ADC clock = 12 MHz Sample time = 55.5 cycles
Total time ≈ (55.5 + 12.5) / 12MHz

## Slide 8: ADC Registers
CR1: • SCAN • AWDEN • AWDIE
CR2: • CONT • DMA • ADON
SQRx: • Channel sequence

## Slide 9: DMA Overview
DMA1 Channel 1 → ADC1
Peripheral-to-Memory
AHB Bus Master
Interrupt capable

## Slide 10: DMA Circular Mode
DMA_CCR1: • CIRC = 1 • MINC = 1 • DIR = 0 • EN = 1
Result: Continuous Buffer Update

## Slide 11: DMA + ADC Interaction
ADC Conversion Complete → Sets EOC → DMA Request Generated → Data moved to SRAM
No CPU Interrupt Needed

## Slide 12: ANALOG WATCHDOG
Integrated Window Comparator
Registers: • ADC_HTR (High Threshold) • ADC_LTR (Low Threshold)

## Slide 13: AWD Interrupt Mechanism
Condition:
ADC_Value > HTR OR ADC_Value < LTR
→ AWD Flag Set → Interrupt to NVIC

## Slide 14: AWD vs IWDG vs WWDG
Analog Watchdog: • Monitors analog signal
IWDG: • Independent watchdog • Resets system if CPU hangs
WWDG: • Window watchdog • Checks refresh timing

## Slide 15: BIT-BANDING
Each Bit → Unique Alias Address
Atomic Operation
No Read-Modify-Write

## Slide 16: Why Bit-Banding Matters
Used For: • Enabling ADC • Enabling DMA • Enabling Interrupt
Prevents Race Conditions

## Slide 17: Autonomous Flow
Sensor ↓ ADC (Continuous + Scan) ↓ DMA (Circular) ↓ Memory
Parallel: Analog Watchdog → CPU Interrupt

## Slide 18: CPU Load Reduction
Without DMA: • CPU handles every sample
With DMA: • CPU handles only exceptions
Efficiency ↑ Power Consumption ↓

## Slide 19: Real-Time Determinism
Hardware-based detection Fixed conversion time No software delay
Suitable for: • Industrial control • Motor systems • Power electronics

## Slide 20: Industrial Applications
Battery Management System
Over-temperature protection
Voltage monitoring
Pressure sensing

## Slide 21: Conclusion
ADC → Converts DMA → Transfers AWD → Protects Bit-Banding → Controls Safely
Together → Intelligent Embedded Monitoring System