## Slide 1
TITLE:
GENERAL PURPOSE INPUT/OUTPUT (GPIO) PINS
Presented by :
Plabon Dey-2210776118
Md. Akibuzzaman-2210976128
Md. Ruhul Amin-2210776147
Mahfuzur Rahman-2110976149
Course name :
Microprocessor and Microcontroller

## Slide 2
Introduction to GPIO
GPIO stands for General Purpose Input/Output, which are programmable pins on a microcontroller used to interact with external devices.
GPIO pins can send or receive digital signals.
They connect the microcontroller to external hardware.
Each pin can be controlled individually using software.
Key Points:
Purpose:
Allows communication between the microcontroller and external components.

## Slide 3
Block Representation of the STM32F103C8T6 Microcontroller Built on the ARM Cortex-M3 Architecture.

## Slide 4
Available Ports
GPIOA, GPIOB, GPIOC, GPIOD, GPIOE
GPIO Ports and Pins in STM32
GPIO pins are organized into ports.
  Each port contains 16 pins.
  Each pin is identified by port name and number.
Example:
  PA0, PA1, PA2 … PA15
  PB0, PB1, PB2 … PB15
Each pin can be configured independently.

## Slide 5
GPIO Operating Modes
GPIO pins support four main modes:
  Input Mode – Reads signals from external devices
  Output Mode – Sends signals to external devices
  Alternate Function Mode – Used for communication peripherals
  Analog Mode – Used for analog signal processing
These modes provide flexibility in hardware interfacing.

## Slide 6
Purpose:
Used to receive signals from external devices.
Input Mode
Applications:
  Reading button input
  Receiving sensor signals
  Detecting digital signals
Example:
  Button pressed → GPIO reads HIGH
  Button released → GPIO reads LOW
  This allows the microcontroller to detect external events.

## Slide 7
Output Mode
Purpose:
Used to send signals to external devices.
Applications:
Example:
  LED control
  Relay control
  Motor control
  Example:
  GPIO HIGH → LED ON
  GPIO LOW → LED OFF
  This allows the microcontroller to control external hardware.

## Slide 8
Alternate Function and Analog Mode
Alternate Function Mode
Used when GPIO works with internal peripherals such as:
  UART ,SPI ,I2C ,Timers ,PWM
Example:
PA2 → UART Transmit
Analog Mode
Used for analog signal processing.
Example:
Reading sensor voltage using ADC

## Slide 9
Pull-Up, Pull-Down and Output Types
Pull-Up and Pull-Down Resistors:
Used to ensure stable input signals.
  Pull-Up → Default HIGH
  Pull-Down → Default LOW
Output Types:
Push-Pull:
  Standard output
  Used for LEDs and general output
Open-Drain:
  Used for communication protocols like I2C

## Slide 10
Common Applications:
  LED control
  Button input
  Sensor interfacing
  Communication interfaces
  Motor control
GPIO Applications and Example
Example:
Steps:
  Configure GPIO pin as output
  Set pin HIGH → LED ON
  Set pin LOW → LED OFF

## Slide 11
Conclusion
  GPIO pins are essential for microcontroller operation.
  They allow communication with external devices.
  GPIO supports multiple modes for different applications.
  GPIO is widely used in embedded systems for control and interfacing.

## Slide 12
Thank you
Md. Akibuzzaman-2210976128
Presented by :
Plabon Dey-2210776118
Md. Ruhul Amin-2210776147
Mahfuzur Rahman-2110976149