## Slide 1: STM32F103C8 Reset and Clock Control (RCC)
Presentation on RCC Module

## Slide 2: Group 5
Saim Ahmed Emon – 2211076105
Md Mehedy Abu hasan Alvi – 2210476110
Md Mosabbir Hossain – 2210576129
Md Ifran khan - 2210776103

## Slide 3: What is RCC?
RCC = Reset and Clock Control
  • Controls clock generation
  • Distributes clock to CPU and peripherals
  • Controls peripheral reset
  • Required for enabling GPIO, USART, ADC etc.

## Slide 4: How RCC Works - Clock Sources
STM32F103C8 has three main clock sources:
  • HSI – Internal 8 MHz clock
  • HSE – External crystal clock
  • PLL – Multiplies frequency
  System clock (SYSCLK) is selected from these.

## Slide 5
How RCC Works
//1. Enable HSE RCC→CR |= (1 << 17); while(!(RCC→CR &(1<<17)));
//2. Configure PLL: HSE as source,9x RCC→CFGR |= (1 << 16); // PLLSRC = HSE
RCC→ CFGR |= (7 << 18); // PLLMUL = 9
//3. Enable PLL
RCC → CR |= (1 << 24);
While(!(RCC→ CR & (1 << 25)));
//4. Select PLL as SYSCLK
RCC → CFGR |= (2 << 0);

## Slide 6: An Example
Before using any GPIO port:
  • Clock must be enabled using RCC
  Example: Enable GPIOA clock
  RCC->APB2ENR |= (1 << 2);
  Without enabling clock, port will not work.

## Slide 7: RCC Registers
RCC_CR → Clock control
RCC_CFGR → Clock configuration
RCC_APB2ENR → APB2 peripheral enable
RCC_APB1ENR → APB1 peripheral enable
RCC_AHBENR → AHB peripheral enable

## Slide 8: Reset Control Using RCC
RCC can reset any peripheral.
Example:
  RCC->APB2RSTR |= (1 << 2); // Reset GPIOA
  RCC->APB2RSTR &= ~(1 << 2); // Release reset

## Slide 9: Power Saving
RCC helps in power management:
  Disable unused ports
  Reduce system clock frequency
This reduces power consumption.

## Slide 10: Conclusion
RCC controls clock and reset
  RCC controls clock generation
  Selects clock source (HSI, HSE, PLL)
  Enables and resets GPIO and other modules
  Helps in power optimization